# Zilog Z80 CPU Specifications
# by Sean Young (syoung@cs.vu.nl)
# Last update: September 21, 1997

# Opcode Prefixes
There are four different opcode prefixes: CB, DD, ED and FD. If an opcode begins the DD prefix, the IX register is used in stead of the HL register and likewise the FD prefix results in use of the IY register in stead of the HL register. If HL refers to memory address, (e.g. LD A, (HL) ), an offset d is added to the opcode (e.g. LD A, (IX + d) ). If the instruction uses the H or L register, the high order byte or the low order byte of the IX or IY register is used. There are two exceptions to this rule, though: the EXX and EX DE, HL instructions. These instructions cannot be changed with a DD or FD prefix. If the instruction does not use the HL, H or L register, the instruction is executed as without the DD or FD prefix (except for the DDCB and FDCB opcode prefixes). Multiple DDs or FDs after each other operate like NOPs. If a instruction is preceded by an ED, a new set of instructions is used (see Opcode list). If the opcode is not listed, it will operate as two NOPs. Similarly the CB, FDCB and the DDCB select a new instruction set, though every possible instruction has a function and is listed.
# The IM 0/1 and RETI/N instructions
The opcode list shows these two strange instructions. They are unofficial, and because both possibilities operate exactly the same way on a MSX, I can not determine which one they are. It is not important on a MSX though, but if anyone knows which one they are, please let me know.
# Registers
The Z80 has the following (accessible) registers:
I, R, A, F, BC, DE, HL, IX, IY, SP, PC, AF’, BC’, DE’ and HL’.

The R register is for memory refresh. It is increased by 1 after every instruction, whereby the CB, DD, DDCB, ED, FD and FDCB prefixes are viewed as separate instructions. Bit 7 is never modified, but it can be changed with LD A,R.

The F register is the flag register. It has the following structure:
Bit 7:	The S flag: if the result of the operation is negative, this flag is high. This is a copy of the MSB of the result of the operation.
Bit 6:	The Z flag: if the result is zero, this flag is high.
Bit 5:	This bit has no official name. Throughout this document it is referred to as ‘b5’. It is a copy of bit 5 of the result of the operation.
Bit 4:	The H flag. This is the carry from bit 3 to bit 4 of the operation. Used with DAA instruction.
Bit 3:	This bit has no official name. Throughout this document it is referred to as ‘b3’. It is a copy of bit 3 of the result of the operation.
Bit 2:	The P/V flag. It contains the overflow (high if two’s complements result does not fit in register) or the parity (parity of number of high bits in result of operation). See description of instructions for which one.
Bit 1:	The N flag. It is high if the last operation was an subtraction, otherwise it was an addition. Used with DAA instruction.
Bit 0:	The C flag. If the result of the operation does not fit in the register, this bit is high.
Sometimes the flags have other meanings. See descriptions of instructions for details.
# Interrupts
There are two types of interrupts: mask-able and non mask-able, and the are two flip-flops associated with interrupts: IFF1 and IFF2. DI resets both and EI sets both. If IFF1 is set then mask-able interrupts are accepted. When an non mask-able interrupt occurs, the IFF1 is reset, so disabling mask-able interrupts. When the CPU returns from a non mask-able interrupt (with RETN) the IFF2 is copied into IFF1 (and thus restored). Only IFF2 can be read (with LD A, I and LD A, R IFF2 is copied into the P/V flag).
MSX Specific: non mask-able interrupts never occur in a MSX, so the two interrupt flip-flops are always identical. Viewing the CPU as though it has one Interrupt flip-flop is not incorrect.
# Interrupt Modes
Interrupt modes can be set with the IM x instructions. They only affect mask-able interrupts. When a mask-able interrupt occurs, the interrupting device must supply a value.
Interrupt Mode 0:
The value the interrupting device supplies is interpreted as an 8 bit opcode which is executed (usually RST p instructions).
Interrupt Mode 1:
A call is made to address 38h. The value the interrupting device supplies is ignored.
Interrupt Mode 2:
A call is made to an address read from address (register I × 256 + value from interrupting device).
MSX Specific: The MSX has one interrupting device (the VDP), which always provides value FFh (instruction RST 38h), so the MSX operates the same in Interrupt Mode 0 as in 1. In IM 2 a call is made to an address read from address (register I × 256 + FFh).
# Instructions Descriptions
## 8 bit Load Group
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No. of / Bytes	No. of M / Cycles	No. of T / States	Comments
LD r, r’	r ¬ r’		• • • • • • • •	01 r r’		1	1	4	r, r’ Reg.
LD p, p’*	p ¬ p’		• • • • • • • •	11 011 101 / 01 p p’	DD	2	2	8	000 B / 001 C
LD q, q’*	q ¬ q’		• • • • • • • •	11 111 101 / 01 q q’	FD	2	2	8	010 D / 011 E
LD r, n	r ¬ n		• • • • • • • •	00 r 110 / ¬ n ®		2	2	7	100 H / 101 L
LD p, n*	p ¬ n		• • • • • • • •	11 011 101 / 00 p 110 / ¬ n ®	DD	3	3	11	111 A / p, p’ Reg.
LD q, n*	q ¬ n		• • • • • • • •	11 111 101 / 00 q 110 / ¬ n ®	FD	3	3	11	000 B / 001 C / 010 D
LD r, (HL)	r ¬ (HL)		• • • • • • • •	01 r 110		1	2	7	011 E
LD r, (IX + d)	r ¬ (IX + d)		• • • • • • • •	11 011 101 / 01 r 110 / ¬ d ®	DD	3	5	19	100 IXH / 101 IXL / 111 A
LD r, (IY + d)	r ¬ (IY + d)		• • • • • • • •	11 111 101 / 01 r 110 / ¬ d ®	FD	3	5	19	q, q’ Req. / 000 B
LD (HL), r	(HL) ¬ r		• • • • • • • •	01 110 r		1	2	7	001 C
LD (IX + d), r	(IX + d) ¬ r		• • • • • • • •	11 011 101 / 01 110 r / ¬ d ®	DD	3	5	19	010 D / 011 E / 100 IYH
LD (IY + d), r	(IY + d) ¬ r		• • • • • • • •	11 111 101 / 01 110 r / ¬ d ®	FD	3	5	19	101 IYL / 111 A
LD (HL), n	(HL) ¬ n		• • • • • • • •	00 110 110 / ¬ n ®	36	2	3	10
LD (IX + d), n	(IX + d) ¬ n		• • • • • • • •	11 011 101 / 00 110 110 / ¬ d ® / ¬ n ®	DD / 36	4	5	19
LD (IY + d), n	(IY + d) ¬ n		• • • • • • • •	11 111 101 / 00 110 110 / ¬ d ® / ¬ n ®	FD / 36	4	5	19
LD A, (BC)	A ¬ (BC)		• • • • • • • •	00 001 010	0A	1	2	7
LD A, (DE)	A ¬ (DE)		• • • • • • • •	00 011 010	1A	1	2	7
LD A, (nn)	A ¬ (nn)		• • • • • • • •	00 111 010 / ¬ n ® / ¬ n ®	3A	3	4	13
LD (BC), A	(BC) ¬ A		• • • • • • • •	00 000 010	02	1	2	7
LD (DE), A	(DE) ¬ A		• • • • • • • •	00 010 010	12	1	2	7
LD (nn), A	(nn) ¬ A		• • • • • • • •	00 110 010 / ¬ n ® / ¬ n ®	32	3	4	13
LD A, I	A ¬ I		b b b 0 b IFF2 0 •	11 101 101 / 01 010 111	ED / 57	2	2	9
LD A, R	A ¬ R		b b b 0 b IFF2 0 •	11 101 101 / 01 011 111	ED / 5F	2	2	9	R is read after it is increased.
LD I, A	I ¬ A		• • • • • • • •	11 101 101 / 01 000 111	ED / 47	2	2	9
LD R, A	R ¬ A		• • • • • • • •	11 101 101 / 01 001 111	ED / 4F	2	2	9	R is written after it is increased.
Notes:		r, r’ means any of the registers A, B, C, D, E, H, L. / p, p’ means any of the registers A, B, C, D, E, IXH, IXL. / q, q’ means any of the registers A, B, C, D, E, IYH, IYL. / ddL, ddH refer to high order and low order eight bits of the register respectively. / * means unofficial instruction.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, / b = flag is set according to the result of the operation, IFF2 = the interrupt flip-flop 2 is copied.

## 16 bit Load Group
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No. of / Bytes	No. of M / Cycles	No. of T / States	Comments
LD dd, nn	dd ¬ nn		• • • • • • • •	00 dd0 001 / ¬ n ® / ¬ n ®		3	3	10	dd Pair / 00 BC / 01 DE
LD IX, nn	IX ¬ nn		• • • • • • • •	11 011 101 / 00 110 001 / ¬ n ® / ¬ n ®	DD / 21	4	4	14	02 HL / 03 SP
LD IY, nn	IY ¬ nn		• • • • • • • •	11 111 101 / 00 110 001 / ¬ n ® / ¬ n ®	FD / 21	4	4	14
LD HL, (nn)	L ¬ (nn) / H ¬ (nn+1)		• • • • • • • •	00 101 010 / ¬ n ® / ¬ n ®	2A	3	5	16
LD dd, (nn)	ddL ¬ (nn) / ddH ¬ (nn+1)		• • • • • • • •	11 101 101 / 01 dd1 011 / ¬ n ® / ¬ n ®	ED	4	6	20
LD IX, (nn)	IXL ¬ (nn) / IXH ¬ (nn+1)		• • • • • • • •	11 011 101 / 00 101 010 / ¬ n ® / ¬ n ®	DD / 2A	4	6	20
LD IY, (nn)	IYL ¬ (nn) / IYH ¬ (nn+1)		• • • • • • • •	11 111 101 / 00 101 010 / ¬ n ® / ¬ n ®	FD / 2A	4	6	20
LD (nn), HL	(nn) ¬ L / (nn+1) ¬ H		• • • • • • • •	00 100 010 / ¬ n ® / ¬ n ®	22	3	5	16
LD (nn), dd	(nn) ¬ ddL / (nn+1) ¬ ddH		• • • • • • • •	11 101 101 / 01 dd0 011 / ¬ n ® / ¬ n ®	DD	4	6	20
LD (nn), IX	(nn) ¬ IXL / (nn+1) ¬ IXH		• • • • • • • •	11 011 101 / 00 100 010 / ¬ n ® / ¬ n ®	DD / 22	4	6	20
LD (nn), IY	(nn) ¬ IYL / (nn+1) ¬ IYH		• • • • • • • •	11 111 101 / 00 100 010 / ¬ n ® / ¬ n ®	FD / 22	4	6	20
LD SP, HL	SP ¬ HL		• • • • • • • •	11 111 001	F9	1	1	6
LD SP, IX	SP ¬ IX		• • • • • • • •	11 011 101 / 11 111 001	DD / F9	2	2	10
LD SP, IY	SP ¬ IY		• • • • • • • •	11 111 101 / 11 111 001	FD / F9	2	2	10
PUSH qq	SP ¬ SP - 1 / (SP) ¬ qqH / SP ¬ SP - 1 / (SP) ¬ qqL		• • • • • • • •	11 qq0 101		1	3	11	qq Pair / 00 BC / 01 DE / 10 HL
PUSH IX	SP ¬ SP - 1 / (SP) ¬ IXH / SP ¬ SP - 1 / (SP) ¬ IXL		• • • • • • • •	11 011 101 / 11 100 101	DD / E5	2	4	15	11 AF
PUSH IY	SP ¬ SP - 1 / (SP) ¬ IYH / SP ¬ SP - 1 / (SP) ¬ IYL		• • • • • • • •	11 111 101 / 11 100 101	FD / E5	2	4	15
POP qq	(SP) ¬ qqL SP ¬ SP + 1 / (SP) ¬ qqH / SP ¬ SP + 1		• • • • • • • •	11 qq0 001		1	3	10
POP IX	(SP) ¬ IXL SP ¬ SP + 1 / (SP) ¬ IXH / SP ¬ SP + 1		• • • • • • • •	11 011 101 / 11 100 001	DD / E1	2	4	14
POP IY	(SP) ¬ IYL SP ¬ SP + 1 / (SP) ¬ IYH / SP ¬ SP + 1		• • • • • • • •	11 111 101 / 11 100 001	FD / E1	2	4	14
Notes:		dd is any of the register pair BC, DE, HL, SP. / qq is any of the register pair BC, DE, HL, AF.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

## Exchange, Block Transfer and Search Groups
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No.of / Bytes	No.of M / Cycles	No.of T / States	Comments
EX DE, HL	DE « HL		• • • • • • • •	11 101 011	EB	1	1	4
EX AF, AF’	AF « AF’		• • • • • • • •	00 001 000	08	1	1	4
EXX	BC « BC’ / DE « DE’ / HL « HL’		• • • • • • • •	11 011 001	D9	1	1	4
EX (SP), HL	(SP+1) « H / (SP) « L		• • • • • • • •	11 100 011	E3	1	5	19
EX (SP), IX	(SP+1) « IXH / (SP) « IXL		• • • • • • • •	11 011 101 / 11 100 011	DD / E3	2	6	23
EX (SP), IY	(SP+1) « IYH / (SP) « IYL		• • • • • • • •	11 111 101 / 11 100 011	FD / E3	2	6	23
LDI	(DE) ¬ (HL) / DE ¬ DE + 1 / HL ¬ HL + 1 / BC ¬ BC - 1		• • b1 0 b2 b3 0 •	11 101 101 / 10 100 000	ED / A0	2	4	16
LDIR	(DE) ¬ (HL) / DE ¬ DE + 1 / HL ¬ HL + 1 / BC ¬ BC - 1 / repeat until: / BC = 0		• • b1 0 b2 0 0 •	11 101 101 / 10 110 000	ED / B0	2 / 2	5 / 4	21 / 16	if BC ¹ 0 / if BC = 0
LDD	(DE) ¬ (HL) / DE ¬ DE - 1 / HL ¬ HL - 1 / BC ¬ BC - 1		• • b1 0 b2 b3 0 •	11 101 101 / 10 101 000	ED / A8	2	4	16
LDDR	(DE) ¬ (HL) / DE ¬ DE - 1 / HL ¬ HL - 1 / BC ¬ BC - 1 / repeat until: / BC = 0		• • b1 0 b2 0 0 •	11 101 101 / 10 111 000	ED / B8	2 / 2	5 / 4	21 / 16	if BC ¹ 0 / if BC = 0
CPI	A - (HL) / HL ¬ HL + 1 / BC ¬ BC -1		b4 b4 b5 b4 b6 b3 1 •	11 101 101 / 10 100 001	ED / A1	2	4	16
CPIR	A - (HL) / HL ¬ HL + 1 / BC ¬ BC -1 / Repeat until: / A = (HL) or / BC = 0		b4 b4 b5 b4 b6 b3 1 •	11 101 101 / 10 110 001	ED / B1	2 / 2	5 / 4	21 / 16	if BC ¹ 0 and / A ¹ (HL). / if BC = 0 or / A = (HL)
CPD	A - (HL) / HL ¬ HL - 1 / BC ¬ BC -1		b4 b4 b5 b4 b6 b3 1 •	11 101 101 / 10 101 001	ED / A9	2	4	16
CPDR	A - (HL) / HL ¬ HL - 1 / BC ¬ BC -1 / Repeat until: / A = (HL) or / BC = 0		b4 b4 b5 b4 b6 b3 1 •	11 101 101 / 10 111 001	ED / B9	2 / 2	5 / 4	21 / 16	if BC ¹ 0 and / A ¹ (HL). / if BC = 0 or / A = (HL)
Notes:		1 F5 is a copy of bit 1 of A + last transferred byte, thus (A + (HL))1 / 2 F3 is a copy of bit 3 of A + last transferred byte, thus (A + (HL))3 / 3 P/V flag is 0 if the result of BC - 1 = 0, otherwise P/V = 1. / 4 These flags are set as in CP (HL) / 5 F5 is copy of bit 1 of A - last compared address - H, thus (A - (HL) - H)1. H is as in F after the comparison. / 6 F3 is copy of bit 3 of A - last compared address - H, thus (A - (HL) - H)3. H is as in F after the comparison.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

## 8 bit Arithmetic and Logical Group
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No.of / Bytes	No.of M / Cycles	No.of T / States	Comments
ADD A, r	A ¬ A + r		b b b b b V 0 b	10 000 r		1	1	4	r Reg. p Reg.
ADD A, p*	A ¬ A + p		b b b b b V 0 b	11 011 101 / 10 000 p	DD	2	2	8	000 B 000 B / 001 C 001 C
ADD A, q*	A ¬ A + q		b b b b b V 0 b	11 111 101 / 10 000 q	FD	2	2	8	010 D 010 D / 011 E 011 E
ADD A, n	A ¬ A + n		b b b b b V 0 b	11 000 110 / ¬ n ®		2	2	8	100 H 100 IXH / 101 L 101 IXH
ADD A, (HL)	A ¬ A + (HL)		b b b b b V 0 b	10 000 110		1	2	7	111 A 111 A
ADD A, (IX + d)	A ¬ A + (IX + d)		b b b b b V 0 b	11 011 101 / 10 000 110 / ¬ d ®	DD	3	5	19
ADD A, (IY + d)	A ¬ A + (IY + d)		b b b b b V 0 b	11 111 101 / 10 000 110 / ¬ d ®	FD	3	5	19
ADC A, s	A ¬ A + s + CY		b b b b b V 0 b	001					s is any of r, n, (HL),
SUB A, s	A ¬ A - s		b b b b b V 1 b	010					(IX+d), (IY+d), p, q
SBC A, s	A ¬ A - s - CY		b b b b b V 1 b	011					as shown for the ADD
AND s	A ¬ A AND s		b b b 1 b P 0 0	100					instruction. The
OR s	A ¬ A OR s		b b b 0 b P 0 0	110					underlined bits replace
XOR s	A ¬ A XOR s		b b b 0 b P 0 0	101					the underlined bits in
CP s	A - s		b b b1 b b1 V 1 b	111					the ADD set.
INC r	r ¬ r + 1		b b b b b V 0 •	00 r 100		1	1	4
INC p*	p ¬ p + 1		b b b b b V 0 •	11 011 101 / 00 p 100	DD	2	2	8	q Reg. / 000 B
INC q*	q ¬ q + 1		b b b b b V 0 •	11 111 101 / 00 q 100	FD	2	2	8	001 C / 010 D
INC (HL)	(HL) ¬ (HL) + 1		b b b b b V 0 •	00 110 100		1	3	11	011 E
INC (IX + d)	(IX + d) ¬ / (IX + d) + 1		b b b b b V 0 •	11 011 101 / 00 110 100 / ¬ d ®	DD	3	6	23	100 IYH / 101 IYL / 111 A
INC (IY + d)	(IY + d) ¬ / (IY + d) + 1		b b b b b V 0 •	11 111 101 / 00 110 100 / ¬ d ®	FD	3	6	23
DEC m	m ¬ m - 1		b b b b b V 1 •	101					m is any of r, p, q, (HL), (IX+d), (IY+d), as shown for the INC instruction. DEC same format and states as INC. Replace 100 with 101 in opcode.
Notes:		1 F5 and F3 are copied from the operand (s), not from the result of (A - s). / The V symbol in the P/V flag column indicates that the P/V flags contains the overflow of the operation. Similarly the P symbol indicates parity. / r means any of the registers A, B, C, D, E, H, L. / p means any of the registers A, B, C, D, E, IXH, IXL. / q means any of the registers A, B, C, D, E, IYH, IYL. / ddL, ddH refer to high order and low order eight bits of the register respectively. / CY means the carry flip-flop. / * means unofficial instruction.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

## 16 bit Arithmetic Group
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No.of / Bytes	No.of M / Cycles	No.of T / States	Comments
ADD HL, ss	HL ¬ HL + ss		• • b2 b2 b2 • 0 b1	00 ss1 001		1	3	11	ss Reg.
ADC HL, ss	HL ¬ HL + ss + CY		b1 b1 b2 b2 b2 V1 0 b1	11 101 101 / 01 ss1 010	ED	2	4	15	00 BC / 01 DE
SBC HL, ss	HL ¬ HL - ss - CY		b1 b1 b2 b2 b2 V1 1 b1	11 101 101 / 01 ss0 010	ED	2	4	15	10 HL / 11 SP
ADD IX, pp	IX ¬ IX + pp		• • b2 b2 b2 • 0 b1	11 011 101 / 00 pp1 001	DD	2	4	15	pp Reg.
ADD IY, rr	IY ¬ IY + rr		• • b2 b2 b2 • 0 b1	11 111 101 / 00 rr1 001	FD	2	4	15	00 BC / 01 DE
INC ss	ss ¬ ss + 1		• • • • • • • •	00 ss0 011		1	1	6	10 IX
INC IX	IX ¬ IX + 1		• • • • • • • •	11 011 101 / 00 100 011	DD / 23	2	2	10	11 SP
INC IY	IY ¬ IY + 1		• • • • • • • •	11 111 101 / 00 100 011	FD / 23	2	2	10	rr Reg. / 00 BC
DEC ss	ss ¬ ss - 1		• • • • • • • •	00 ss1 011		1	1	6	01 DE
DEC IX	IX ¬ IX - 1		• • • • • • • •	11 011 101 / 00 101 011	DD / 2B	2	2	10	10 IY / 11 SP
DEC IY	IY ¬ IY - 1		• • • • • • • •	11 111 101 / 00 101 011	FD / 2B	2	2	10
Notes:		The V symbol in the P/V flag column indicates that the P/V flags contains the overflow of the operation. / ss means any of the registers BC, DE, HL, SP. / pp means any of the registers BC, DE, IX, SP. / rr means any of the registers BC, DE, IY, SP. / 16 bit additions are performed by first adding the two low order eight bits, and then the two high order eight bits. / 1 Indicates the flag is affected by the 16 bit result of the operation. / 2 Indicates the flag is affected by the 8 bit addition of the high order eight bits. / CY means the carry flip-flop.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

## General Purpose Arithmetic and CPU Control Groups
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No.of / Bytes	No.of M / Cycles	No.of T / States	Comments
DAA	Converts A into packed BCD following add or subtract with BCD operands. / __		b b b b b P • b	00 100 111	27	1	1	4
CPL	A ¬ A		• • b1 1 b1 • 1 •	00 101 111	2F	1	1	4	One’s complement.
NEG4	A ¬ 0 - A / __		b b b b b V 1 b	11 101 101 / 01 000 100	ED / 44	2	2	8	Two’s complement.
CCF	CY ¬ CY		• • b1 b2 b1 • 0 b	00 111 111	3F	1	1	4	Complement carry flag.
SCF	CY ¬ 1		• • b1 0 b1 • 0 1	00 110 111	37	1	1	4
NOP	No operations		• • • • • • • •	00 000 000	00	1	1	4
HALT	CPU halted		• • • • • • • •	01 110 110	76	1	1	4
DI3	IFF1 ¬ 0 / IFF2 ¬ 0		• • • • • • • •	11 110 011	F3	1	1	4
EI3	IFF1 ¬ 1 / IFF2 ¬ 1		• • • • • • • •	11 111 011	FB	1	1	4
IM 04	Set interrupt mode 0		• • • • • • • •	11 101 101 / 01 000 110	ED / 46	2	2	8
IM 14	Set interrupt mode 1		• • • • • • • •	11 101 101 / 01 010 110	ED / 56	2	2	8
IM 24	Set interrupt mode 2		• • • • • • • •	11 101 101 / 01 011 110	ED / 5E	2	2	8
Notes:		The V symbol in the P/V flag column indicates that the P/V flags contains the overflow of the operation. Similarly the P symbol indicates parity. / 1 F5 and F3 are a copy of bit 5 and 3 of register A _ / 2 H contains the previous carry state (after instruction H « C) / 3 No interrupts are issued directly after a DI or EI. / 4 This instruction has other unofficial opcodes, see Opcodes list. / CY means the carry flip-flop.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

## Rotate and Shift Group
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No. of / Bytes	No. of M / Cycles	No. of T / States	Comments
RLCA			• • b 0 b • 0 b	00 000 111	07	1	1	4
RLA			• • b 0 b • 0 b	00 010 111	17	1	1	4
RRCA			• • b 0 b • 0 b	00 001 111	0F	1	1	4
RRA			• • b 0 b • 0 b	00 011 111	1F	1	1	4
RLC r			b b b 0 b P 0 b	11 001 011 / 00 000 r	CB	2	2	8	r Reg. / 000 B
RLC (HL)			b b b 0 b P 0 b	11 001 011 / 00 000 110	CB	2	4	15	001 C / 010 D
RLC (IX + d)			b b b 0 b P 0 b	11 011 101 / 11 001 011 / ¬ d ® / 00 000 110	DD / CB	4	6	23	011 E / 100 H / 101 L / 111 A
RLC (IY + d)			b b b 0 b P 0 b	11 111 101 / 11 001 011 / ¬ d ® / 00 000 110	FD / CB	4	6	23
LD r,RLC (IX + d)*	r ¬ (IX + d) / RLC r / (IX + d) ¬ r		b b b 0 b P 0 b	11 011 101 / 11 001 011 / ¬ d ® / 00 000 r	DD / CB	4	6	23
LD r,RLC (IY + d)*	r ¬ (IY + d) / RLC r / (IY + d) ¬ r		b b b 0 b P 0 b	11 111 101 / 11 001 011 / ¬ d ® / 00 000 r	FD / CB	4	6	23
RL m			b b b 0 b P 0 b	010					Instruction format
RRC m			b b b 0 b P 0 b	001					and states are the
RR m			b b b 0 b P 0 b	011					same as RLC.
SLA m			b b b 0 b P 0 b	100					Replace 000 with
SLL m*			b b b 0 b P 0 b	110					new number.
SRA m			b b b 0 b P 0 b	101
SRL m			b b b 0 b P 0 b	111
RLD			b b b 0 b P 0 •	11 101 101 / 01 101 111	ED / 6F	2	5	18
RRD			b b b 0 b P 0 •	11 101 101 / 01 100 111	ED / 67	2	5	18
Notes:		The P symbol in the P/V flag column indicates that the P/V flags contains the parity of the result. / r means any of the registers A, B, C, D, E, H, L. / * means unofficial instruction. / CY means the carry flip-flop.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

## Bit Manipulation Group
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No. of / Bytes	No. of M / Cycles	No. of T / States	Comments
BIT b, r	_ / Z ¬ rb		b1 b b2 1 b3 b4 0 •	11 001 011 / 01 b r	CB	2	2	8	r Reg. / 000 B
BIT b, (HL)	___ / Z ¬ (HL)b		b1 b b2 1 b3 b4 0 •	11 001 011 / 01 b 110	CB	2	3	12	001 C / 010 D
BIT b, (IX + d)5	_____ / Z ¬ (IX + d)b		b1 b b2 1 b3 b4 0 •	11 011 101 / 11 001 011 / ¬ d ® / 01 b 110	DD / CB	4	5	20	011 E / 100 H / 101 L / 111 A
BIT b, (IY + d)5	_____ / Z ¬ (IY + d)b		b1 b b2 1 b3 b4 0 •	11 111 101 / 11 001 011 / ¬ d ® / 01 b 110	FD / CB	4	5	20
SET b, r	rb ¬ 1		• • • • • • • •	11 001 011 / 11 b r	CB	2	2	8	b Bit. / 000 0 / 001 1
SET b, (HL)	(HL)b ¬ 1		• • • • • • • •	11 001 011 / 11 b 110	CB	2	4	15	010 2 / 011 3
SET b, (IX + d)	(IX + d)b ¬ 1		• • • • • • • •	11 011 101 / 11 001 011 / ¬ d ® / 11 b 110	DD / CB	4	6	23	100 4 / 101 5 / 110 6 / 111 7
SET b, (IY + d)	(IY + d)b ¬ 1		• • • • • • • •	11 111 101 / 11 001 011 / ¬ d ® / 11 b 110	FD / CB	4	6	23
LD r,SET b, (IX + d)*	r ¬ (IX + d) / rb ¬ 1 / (IX + d) ¬ r		• • • • • • • •	11 011 101 / 11 001 011 / ¬ d ® / 11 b r	DD / CB	4	6	23
LD r,SET b, (IY + d)*	r ¬ (IY + d) / rb ¬ 1 / (IY + d) ¬ r		• • • • • • • •	11 111 101 / 11 001 011 / ¬ d ® / 11 b r	FD / CB	4	6	23
RES b, m	mb ¬ 0 / m º r, (HL), (IX+d), / (IY+d)		• • • • • • • •	10					To form new opcode replace 11 of SET b, s with 10. Flags and states are the same.
Notes:		The notation mb indicates bit b (0 to 7) of location m. / BIT instructions are performed by an bitwise AND. / 1 S is set if b = 7 and Z = 0 / 2 F5 is set if b = 5 and Z = 0 / 3 F3 is set if b = 3 and Z = 0 / 4 P/V is set like the Z flag / 5 This instruction has other unofficial opcodes / * means unofficial instruction.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

## Input and Output Groups
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No.of / Bytes	No.of M / Cycles	No.of T / States	Comments
IN A, (n)	A ¬ (n)		• • • • • • • •	11 011 011 / ¬ n ®	DB	2	3	11	r Reg. / 000 B
IN r, (C)	r ¬ (C)		b b b 0 b P 0 •	11 101 101 / 01 r 000	ED	2	3	12	001 C / 010 D
IN (C)* or / IN F, (C)*	Just affects flags, / value is lost.		b b b 0 b P 0 •	11 101 101 / 01 110 000	ED / 70	2	3	12	011 E / 100 H
INI	(HL) ¬ (C) / HL ¬ HL + 1 / B ¬ B - 1		b1 b1 b1 b3 b1 X b2 b3	11 101 101 / 10 100 010	ED / A2	2	4	16	101 L / 111 A
INIR	(HL) ¬ (C) / HL ¬ HL + 1 / B ¬ B - 1 / Repeat until / B = 0		0 1 0 b3 0 X b2 b3	11 101 101 / 10 110 010	ED / B2	2 / 2	5 / 4	21 / 16	if B ¹ 0 / if B = 0
IND	(HL) ¬ (C) / HL ¬ HL - 1 / B ¬ B - 1		b1 b1 b1 b4 b1 X b2 b4	11 101 101 / 10 101 010	ED / AA	2	4	16
INDR	(HL) ¬ (C) / HL ¬ HL - 1 / B ¬ B - 1 / Repeat until / B = 0		0 1 0 b4 0 X b2 b4	11 101 101 / 10 111 010	ED / BA	2 / 2	5 / 4	21 / 16	if B ¹ 0 / if B = 0
OUT (n), A	(n) ¬ A		• • • • • • • •	11 010 011 / ¬ n ®	D3	2	3	11
OUT (C), r	(C) ¬ r		• • • • • • • •	11 101 101 / 01 r 001	ED	2	3	12
OUT (C), 0*	(C) ¬ 0		• • • • • • • •	11 101 101 / 01 110 001	ED / 71	2	3	12
OUTI	(C) ¬ (HL) / HL ¬ HL + 1 / B ¬ B - 1		b1 b1 b1 X b1 X X X	11 101 101 / 10 100 011	ED / A3	2	4	16
OTIR	(C) ¬ (HL) / HL ¬ HL + 1 / B ¬ B - 1 / Repeat until / B = 0		0 1 0 X 0 X X X	11 101 101 / 10 110 011	ED / B3	2 / 2	5 / 4	21 / 16	if B ¹ 0 / if B = 0
OUTD	(C) ¬ (HL) / HL ¬ HL - 1 / B ¬ B - 1		b1 b1 b1 X b1 X X X	11 101 101 / 10 101 011	ED / AB	2	4	16
OTDR	(C) ¬ (HL) / HL ¬ HL - 1 / B ¬ B - 1 / Repeat until / B = 0		0 1 0 X 0 X X X	11 101 101 / 10 111 011	ED / BB	2 / 2	5 / 4	21 / 16	if B ¹ 0 / if B = 0
Notes:		The V symbol in the P/V flag column indicates that the P/V flags contains the overflow of the operation. Similarly the P symbol indicates parity. / r means any of the registers A, B, C, D, E, H, L. / 1 flag is affected by the result of B ¬ B - 1 as in DEC B. / 2 N is a copy bit 7 of the last value from the input (C). / 3 this flag contains the carry of ( ( (C + 1) AND 255) + (C) ) / 4 this flag contains the carry of ( ( (C - 1) AND 255) + (C) ) / * means unofficial instruction.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, X = flag is unknown, / b = flag is set according to the result of the operation.

## Jump Group
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No.of / Bytes	No.of M / Cycles	No.of T / States	Comments
JP nn	PC ¬ nn		• • • • • • • •	11 000 011 / ¬ n ® / ¬ n ®	C3	3	3	10
JP cc, nn	if cc is true, / PC ¬ nn		• • • • • • • •	11 ccc 010 / ¬ n ® / ¬ n ®		3	3	10	ccc Condition / 000 NZ / 001 Z / 010 NC / 011 C / 100 PO / 101 PE / 110 P
JR e	PC ¬ PC + e		• • • • • • • •	00 011 000 / ¬ e - 2 ®	18	2	3	12	111 M
JR ss, e	if ss is true / PC ¬ PC + e		• • • • • • • •	00 ss 000 / ¬ e - 2 ®		2 / 2	3 / 2	12 / 7	if ss is true / if ss is false
JP HL	PC ¬ HL		• • • • • • • •	11 101 001	E9	1	1	4
JP IX	PC ¬ IX		• • • • • • • •	11 011 101 / 11 101 001	DD / E9	2	2	8	ss Condition 111 C / 110 NC
JP IY	PC ¬ IY		• • • • • • • •	11 111 101 / 11 101 001	FD / E9	2	2	8	101 Z / 100 NZ
DJNZ e	B ¬ B - 1 / if B ¹ 0 / PC ¬ PC + e		• • • • • • • •	00 010 000 / ¬ e - 2 ®	10	2 / 2	2 / 3	8 / 13	if B = 0 / if B ¹ 0
Notes:		e is a signed two-complement number in the range <-126, 129> / e - 2 in the opcode provides an effective number of PC + e as PC incremented by 2 prior to the addition of e.
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

## Call and Return Group
Mnemonic	Symbolic / Operation		Flags / S Z F5 H F3 P/V N C	Opcode / 76 543 210	Hex	No.of / Bytes	No.of M / Cycles	No.of T / States	Comments
CALL nn	SP ¬ SP - 1 / (SP) ¬ PCH / SP ¬ SP - 1 / (SP) ¬ PCL / PC ¬ nn		• • • • • • • •	11 001 101 / ¬ n ® / ¬ n ®	CD	3	5	17
CALL cc, nn	if cc is true, / SP ¬ SP - 1 / (SP) ¬ PCH / SP ¬ SP - 1 / (SP) ¬ PCL / PC ¬ nn		• • • • • • • •	11 ccc 100 / ¬ n ® / ¬ n ®		3 / 3	3 / 5	10 / 17	if cc is false / if cc is true
RET	PCL ¬ (SP) / SP ¬ SP + 1 / PCH ¬ (SP) / SP ¬ SP + 1		• • • • • • • •	11 001 001	C9	1	3	10
RET cc	if cc is true, / PCL ¬ (SP) / SP ¬ SP + 1 / PCH ¬ (SP) / SP ¬ SP + 1		• • • • • • • •	11 ccc 000		1 / 1	1 / 3	5 / 11	if cc is false / if cc is true
RETI2	PCL ¬ (SP) / SP ¬ SP + 1 / PCH ¬ (SP) / SP ¬ SP + 1		• • • • • • • •	11 101 101 / 01 001 101	ED / 4D	2	4	14	cc Condition / 000 NZ / 001 Z / 010 NC / 011 C
RETN1,2	PCL ¬ (SP) / SP ¬ SP + 1 / PCH ¬ (SP) / SP ¬ SP + 1 / IFF1 ¬ IFF2		• • • • • • • •	11 101 101 / 01 000 101	ED / 45	2	4	14	100 PO / 101 PE / 110 P / 111 M
RST p	SP ¬ SP - 1 / (SP) ¬ PCH / SP ¬ SP - 1 / (SP) ¬ PCL / PC ¬ p		• • • • • • • •	11 t 111		1	3	11	t p / 000 0h / 001 8h / 010 10h / 011 18h / 100 20h / 101 28h / 110 30h / 111 38h
Notes:		1 This instruction has other unofficial opcodes, see Opcode list. / 2 Instruction also IFF1 ¬ IFF2
Flag Notation:		• = flag is not affected, 0 = flag is reset, 1 = flag is set, b = flag is set according to the result of the operation.

# Instructions sorted by opcode

If an EDxx instruction is not listed, it should operate as two NOPs.
If a DDxx or FDxx instruction is not listed, it should operate as without the DD or FD prefix.
An asterisk (*) after a instruction means it is unofficial.

00	NOP
01 n n	LD BC, nn
02	LD (BC), A
03	INC BC
04	INC B
05	DEC B
06 n	LD B, n
07	RLCA
08	EX AF, AF’
09	ADD HL, BC
0A	LD A, (BC)
0B	DEC BC
0C	INC C
0D	DEC C
0E n	LD C, n
0F	RRCA
10 n	DJNZ PC + n
11 n n	LD DE, nn
12	LD (DE), A
13	INC DE
14	INC D
15	DEC D
16 n	LD D, n
17	RLA
18 n	JR PC + n
19	ADD HL, DE
1A	LD A, (DE)
1B	DEC DE
1C	INC E
1D	DEC E
1E n	LD E, n
1F	RRA
20 n	JR NZ, PC + n
21 n n	LD HL, nn
22 n n	LD (nn), HL
23	INC HL
24	INC H
25	DEC H
26 n	LD H, n
27	DAA
28 n	JR Z, PC + n
29	ADD HL, HL
2A n n	LD HL, (nn)
2B	DEC HL
2C	INC L
2D	DEC L
2E n	LD L, n
2F	CPL
30 n	JR NC, PC + n
31 n n	LD SP, nn
32 n n	LD (nn), A
33	INC SP
34	INC (HL)
35	DEC (HL)
36 n	LD (HL), n
37	SCF
38 n	JR C, PC + n
39	ADD HL, SP
3A n n	LD A, (nn)
3B	DEC SP
3C	INC A
3D	DEC A
3E n	LD A, n
3F	CCF
40	LD B, B
41	LD B, C
42	LD B, D
43	LD B, E
44	LD B, H
45	LD B, L
46	LD B, (HL)
47	LD B, A
48	LD C, B
49	LD C, C
4A	LD C, D
4B	LD C, E
4C	LD C, H
4D	LD C, L
4E	LD C, (HL)
4F	LD C, A
50	LD D, B
51	LD D, C
52	LD D, D
53	LD D, E
54	LD D, H
55	LD D, L
56	LD D, (HL)
57	LD D, A
58	LD E, B
59	LD E, C
5A	LD E, D
5B	LD E, E
5C	LD E, H
5D	LD E, L
5E	LD E, (HL)
5F	LD E, A
60	LD H, B
61	LD H, C
62	LD H, D
63	LD H, E
64	LD H, H
65	LD H, L
66	LD H, (HL)
67	LD H, A
68	LD L, B
69	LD L, C
6A	LD L, D
6B	LD L, E
6C	LD L, H
6D	LD L, L
6E	LD L, (HL)
6F	LD L, A
70	LD (HL), B
71	LD (HL), C
72	LD (HL), D
73	LD (HL), E
74	LD (HL), H
75	LD (HL), L
76	HALT
77	LD (HL), A
78	LD A, B
79	LD A, C
7A	LD A, D
7B	LD A, E
7C	LD A, H
7D	LD A, L
7E	LD A, (HL)
7F	LD A, A
80	ADD A, B
81	ADD A, C
82	ADD A, D
83	ADD A, E
84	ADD A, H
85	ADD A, L
86	ADD A, (HL)
87	ADD A, A
88	ADC A, B
89	ADC A, C
8A	ADC A, D
8B	ADC A, E
8C	ADC A, H
8D	ADC A, L
8E	ADC A, (HL)
8F	ADC A, A
90	SUB B
91	SUB C
92	SUB D
93	SUB E
94	SUB H
95	SUB L
96	SUB (HL)
97	SUB A
98	SBC A, B
99	SBC A, C
9A	SBC A, D
9B	SBC A, E
9C	SBC A, H
9D	SBC A, L
9E	SBC A, (HL)
9F	SBC A, A
A0	AND B
A1	AND C
A2	AND D
A3	AND E
A4	AND H
A5	AND L
A6	AND (HL)
A7	AND A
A8	XOR B
A9	XOR C
AA	XOR D
AB	XOR E
AC	XOR H
AD	XOR L
AE	XOR (HL)
AF	XOR A
B0	OR B
B1	OR C
B2	OR D
B3	OR E
B4	OR H
B5	OR L
B6	OR (HL)
B7	OR A
B8	CP B
B9	CP C
BA	CP D
BB	CP E
BC	CP H
BD	CP L
BE	CP (HL)
BF	CP A
C0	RET NZ
C1	POP BC
C2 n n	JP NZ, nn
C3 n n	JP nn
C4 n n	CALL NZ, nn
C5	PUSH BC
C6 n	ADD A, n
C7	RST 0h
C8	RET Z
C9	RET
CA n n	JP Z, nn
CB00	RLC B
CB01	RLC C
CB02	RLC D
CB03	RLC E
CB04	RLC H
CB05	RLC L
CB06	RLC (HL)
CB07	RLC A
CB08	RRC B
CB09	RRC C
CB0A	RRC D
CB0B	RRC E
CB0C	RRC H
CB0D	RRC L
CB0E	RRC (HL)
CB0F	RRC A
CB10	RL B
CB11	RL C
CB12	RL D
CB13	RL E
CB14	RL H
CB15	RL L
CB16	RL (HL)
CB17	RL A
CB18	RR B
CB19	RR C
CB1A	RR D
CB1B	RR E
CB1C	RR H
CB1D	RR L
CB1E	RR (HL)
CB1F	RR A
CB20	SLA B
CB21	SLA C
CB22	SLA D
CB23	SLA E
CB24	SLA H
CB25	SLA L
CB26	SLA (HL)
CB27	SLA A
CB28	SRA B
CB29	SRA C
CB2A	SRA D
CB2B	SRA E
CB2C	SRA H
CB2D	SRA L
CB2E	SRA (HL)
CB2F	SRA A
CB30	SLL B*
CB31	SLL C*
CB32	SLL D*
CB33	SLL E*
CB34	SLL H*
CB35	SLL L*
CB36	SLL (HL)*
CB37	SLL A*
CB38	SRL B
CB39	SRL C
CB3A	SRL D
CB3B	SRL E
CB3C	SRL H
CB3D	SRL L
CB3E	SRL (HL)
CB3F	SRL A
CB40	BIT 0, B
CB41	BIT 0, C
CB42	BIT 0, D
CB43	BIT 0, E
CB44	BIT 0, H
CB45	BIT 0, L
CB46	BIT 0, (HL)
CB47	BIT 0, A
CB48	BIT 1, B
CB49	BIT 1, C
CB4A	BIT 1, D
CB4B	BIT 1, E
CB4C	BIT 1, H
CB4D	BIT 1, L
CB4E	BIT 1, (HL)
CB4F	BIT 1, A
CB50	BIT 2, B
CB51	BIT 2, C
CB52	BIT 2, D
CB53	BIT 2, E
CB54	BIT 2, H
CB55	BIT 2, L
CB56	BIT 2, (HL)
CB57	BIT 2, A
CB58	BIT 3, B
CB59	BIT 3, C
CB5A	BIT 3, D
CB5B	BIT 3, E
CB5C	BIT 3, H
CB5D	BIT 3, L
CB5E	BIT 3, (HL)
CB5F	BIT 3, A
CB60	BIT 4, B
CB61	BIT 4, C
CB62	BIT 4, D
CB63	BIT 4, E
CB64	BIT 4, H
CB65	BIT 4, L
CB66	BIT 4, (HL)
CB67	BIT 4, A
CB68	BIT 5, B
CB69	BIT 5, C
CB6A	BIT 5, D
CB6B	BIT 5, E
CB6C	BIT 5, H
CB6D	BIT 5, L
CB6E	BIT 5, (HL)
CB6F	BIT 5, A
CB70	BIT 6, B
CB71	BIT 6, C
CB72	BIT 6, D
CB73	BIT 6, E
CB74	BIT 6, H
CB75	BIT 6, L
CB76	BIT 6, (HL)
CB77	BIT 6, A
CB78	BIT 7, B
CB79	BIT 7, C
CB7A	BIT 7, D
CB7B	BIT 7, E
CB7C	BIT 7, H
CB7D	BIT 7, L
CB7E	BIT 7, (HL)
CB7F	BIT 7, A
CB80	RES 0, B
CB81	RES 0, C
CB82	RES 0, D
CB83	RES 0, E
CB84	RES 0, H
CB85	RES 0, L
CB86	RES 0, (HL)
CB87	RES 0, A
CB88	RES 1, B
CB89	RES 1, C
CB8A	RES 1, D
CB8B	RES 1, E
CB8C	RES 1, H
CB8D	RES 1, L
CB8E	RES 1, (HL)
CB8F	RES 1, A
CB90	RES 2, B
CB91	RES 2, C
CB92	RES 2, D
CB93	RES 2, E
CB94	RES 2, H
CB95	RES 2, L
CB96	RES 2, (HL)
CB97	RES 2, A
CB98	RES 3, B
CB99	RES 3, C
CB9A	RES 3, D
CB9B	RES 3, E
CB9C	RES 3, H
CB9D	RES 3, L
CB9E	RES 3, (HL)
CB9F	RES 3, A
CBA0	RES 4, B
CBA1	RES 4, C
CBA2	RES 4, D
CBA3	RES 4, E
CBA4	RES 4, H
CBA5	RES 4, L
CBA6	RES 4, (HL)
CBA7	RES 4, A
CBA8	RES 5, B
CBA9	RES 5, C
CBAA	RES 5, D
CBAB	RES 5, E
CBAC	RES 5, H
CBAD	RES 5, L
CBAE	RES 5, (HL)
CBAF	RES 5, A
CBB0	RES 6, B
CBB1	RES 6, C
CBB2	RES 6, D
CBB3	RES 6, E
CBB4	RES 6, H
CBB5	RES 6, L
CBB6	RES 6, (HL)
CBB7	RES 6, A
CBB8	RES 7, B
CBB9	RES 7, C
CBBA	RES 7, D
CBBB	RES 7, E
CBBC	RES 7, H
CBBD	RES 7, L
CBBE	RES 7, (HL)
CBBF	RES 7, A
CBC0	SET 0, B
CBC1	SET 0, C
CBC2	SET 0, D
CBC3	SET 0, E
CBC4	SET 0, H
CBC5	SET 0, L
CBC6	SET 0, (HL)
CBC7	SET 0, A
CBC8	SET 1, B
CBC9	SET 1, C
CBCA	SET 1, D
CBCB	SET 1, E
CBCC	SET 1, H
CBCD	SET 1, L
CBCE	SET 1, (HL)
CBCF	SET 1, A
CBD0	SET 2, B
CBD1	SET 2, C
CBD2	SET 2, D
CBD3	SET 2, E
CBD4	SET 2, H
CBD5	SET 2, L
CBD6	SET 2, (HL)
CBD7	SET 2, A
CBD8	SET 3, B
CBD9	SET 3, C
CBDA	SET 3, D
CBDB	SET 3, E
CBDC	SET 3, H
CBDD	SET 3, L
CBDE	SET 3, (HL)
CBDF	SET 3, A
CBE0	SET 4, B
CBE1	SET 4, C
CBE2	SET 4, D
CBE3	SET 4, E
CBE4	SET 4, H
CBE5	SET 4, L
CBE6	SET 4, (HL)
CBE7	SET 4, A
CBE8	SET 5, B
CBE9	SET 5, C
CBEA	SET 5, D
CBEB	SET 5, E
CBEC	SET 5, H
CBED	SET 5, L
CBEE	SET 5, (HL)
CBEF	SET 5, A
CBF0	SET 6, B
CBF1	SET 6, C
CBF2	SET 6, D
CBF3	SET 6, E
CBF4	SET 6, H
CBF5	SET 6, L
CBF6	SET 6, (HL)
CBF7	SET 6, A
CBF8	SET 7, B
CBF9	SET 7, C
CBFA	SET 7, D
CBFB	SET 7, E
CBFC	SET 7, H
CBFD	SET 7, L
CBFE	SET 7, (HL)
CBFF	SET 7, A
CC n n	CALL Z, nn
CD n n	CALL nn
CE n	ADC A, n
CF	RST 8h
D0	RET NC
D1	POP DE
D2 n n	JP NC, nn
D3 n	OUT (n), A
D4 n n	CALL NC, nn
D5	PUSH DE
D6 n	SUB n
D7	RST 10h
D8	RETC
D9	EXX
DA n n	JP C, nn
DB n	IN A, (n)
DC n n	CALL C, nn
DD09	ADD IX, BC
DD19	ADD IX, DE
DD21 n n	LD IX, nn
DD22 n n	LD (nn), IX
DD23	INC IX
DD24	INC IXH*
DD25	DEC IXH*
DD26 n	LD IXH, n*
DD29	ADD IX, IX
DD2A n n	LD IX, (nn)
DD2B	DEC IX
DD2C	INC IXL*
DD2D	DEC IXL*
DD2E n	LD IXL, n*
DD34 d	INC (IX + d)
DD35 d	DEC (IX + d)
DD36 d n	LD (IX + d), n
DD39	ADD IX, SP
DD44	LD B, IXH*
DD45	LD B, IXL*
DD46 d	LD B, (IX + d)
DD4C	LD C, IXH*
DD4D	LD C, IXL*
DD4E d	LD C, (IX + d)
DD54	LD D, IXH*
DD55	LD D, IXL*
DD56 d	LD D, (IX + d)
DD5C	LD E, IXH*
DD5D	LD E, IXL*
DD5E d	LD E, (IX + d)
DD60	LD IXH, B*
DD61	LD IXH, C*
DD62	LD IXH, D*
DD63	LD IXH, E*
DD64	LD IXH, IXH*
DD65	LD IXH, IXL*
DD66 d	LD H, (IX + d)
DD67	LD IXH, A*
DD68	LD IXL, B*
DD69	LD IXL, C*
DD6A	LD IXL, D*
DD6B	LD IXL, E*
DD6C	LD IXL, IXH*
DD6D	LD IXL, IXL*
DD6E d	LD L, (IX + d)
DD6F	LD IXL, A*
DD70 d	LD (IX + d), B
DD71 d	LD (IX + d), C
DD72 d	LD (IX + d), D
DD73 d	LD (IX + d), E
DD74 d	LD (IX + d), H
DD75 d	LD (IX + d), L
DD77 d	LD (IX + d), A
DD7C	LD A, IXH*
DD7D	LD A, IXL*
DD7E d	LD A, (IX + d)
DD84	ADD A, IXH*
DD85	ADD A, IXL*
DD86 d	ADD A, (IX + d)
DD8C	ADC A, IXH*
DD8D	ADC A, IXL*
DD8E d	ADC A, (IX + d)
DD94	SUB IXH*
DD95	SUB IXL*
DD96 d	SUB (IX + d)
DD9C	SBC A, IXH*
DD9D	SBC A, IXL*
DD9E d	SBC A, (IX + d)
DDA4	AND IXH*
DDA5	AND IXL*
DDA6 d	AND (IX + d)
DDAC	XOR IXH*
DDAD	XOR IXL*
DDAE d	XOR (IX + d)
DDB4	OR IXH*
DDB5	OR IXL*
DDB6 d	OR (IX + d)
DDBC	CP IXH*
DDBD	CP IXL*
DDBE d	CP (IX + d)
DDCB d 00	LD B, RLC (IX + d)*
DDCB d 01	LD C, RLC (IX + d)*
DDCB d 02	LD D, RLC (IX + d)*
DDCB d 03	LD E, RLC (IX + d)*
DDCB d 04	LD H, RLC (IX + d)*
DDCB d 05	LD L, RLC (IX + d)*
DDCB d 06	RLC (IX + d)
DDCB d 07	LD A, RLC (IX + d)*
DDCB d 08	LD B, RRC (IX + d)*
DDCB d 09	LD C, RRC (IX + d)*
DDCB d 0A	LD D, RRC (IX + d)*
DDCB d 0B	LD E, RRC (IX + d)*
DDCB d 0C	LD H, RRC (IX + d)*
DDCB d 0D	LD L, RRC (IX + d)*
DDCB d 0E	RRC (IX + d)
DDCB d 0F	LD A, RRC (IX + d)*
DDCB d 10	LD B, RL (IX + d)*
DDCB d 11	LD C, RL (IX + d)*
DDCB d 12	LD D, RL (IX + d)*
DDCB d 13	LD E, RL (IX + d)*
DDCB d 14	LD H, RL (IX + d)*
DDCB d 15	LD L, RL (IX + d)*
DDCB d 16	RL (IX + d)
DDCB d 17	LD A, RL (IX + d)*
DDCB d 18	LD B, RR (IX + d)*
DDCB d 19	LD C, RR (IX + d)*
DDCB d 1A	LD D, RR (IX + d)*
DDCB d 1B	LD E, RR (IX + d)*
DDCB d 1C	LD H, RR (IX + d)*
DDCB d 1D	LD L, RR (IX + d)*
DDCB d 1E	RR (IX + d)
DDCB d 1F	LD A, RR (IX + d)*
DDCB d 20	LD B, SLA (IX + d)*
DDCB d 21	LD C, SLA (IX + d)*
DDCB d 22	LD D, SLA (IX + d)*
DDCB d 23	LD E, SLA (IX + d)*
DDCB d 24	LD H, SLA (IX + d)*
DDCB d 25	LD L, SLA (IX + d)*
DDCB d 26	SLA (IX + d)
DDCB d 27	LD A, SLA (IX + d)*
DDCB d 28	LD B, SRA (IX + d)*
DDCB d 29	LD C, SRA (IX + d)*
DDCB d 2A	LD D, SRA (IX + d)*
DDCB d 2B	LD E, SRA (IX + d)*
DDCB d 2C	LD H, SRA (IX + d)*
DDCB d 2D	LD L, SRA (IX + d)*
DDCB d 2E	SRA (IX + d)
DDCB d 2F	LD A, SRA (IX + d)*
DDCB d 30	LD B, SLL (IX + d)*
DDCB d 31	LD C, SLL (IX + d)*
DDCB d 32	LD D, SLL (IX + d)*
DDCB d 33	LD E, SLL (IX + d)*
DDCB d 34	LD H, SLL (IX + d)*
DDCB d 35	LD L, SLL (IX + d)*
DDCB d 36	SLL (IX + d)*
DDCB d 37	LD A, SLL (IX + d)*
DDCB d 38	LD B, SRL (IX + d)*
DDCB d 39	LD C, SRL (IX + d)*
DDCB d 3A	LD D, SRL (IX + d)*
DDCB d 3B	LD E, SRL (IX + d)*
DDCB d 3C	LD H, SRL (IX + d)*
DDCB d 3D	LD L, SRL (IX + d)*
DDCB d 3E	SRL (IX + d)
DDCB d 3F	LD A, SRL (IX + d)*
DDCB d 40	BIT 0, (IX + d)*
DDCB d 41	BIT 0, (IX + d)*
DDCB d 42	BIT 0, (IX + d)*
DDCB d 43	BIT 0, (IX + d)*
DDCB d 44	BIT 0, (IX + d)*
DDCB d 45	BIT 0, (IX + d)*
DDCB d 46	BIT 0, (IX + d)
DDCB d 47	BIT 0, (IX + d)*
DDCB d 48	BIT 1, (IX + d)*
DDCB d 49	BIT 1, (IX + d)*
DDCB d 4A	BIT 1, (IX + d)*
DDCB d 4B	BIT 1, (IX + d)*
DDCB d 4C	BIT 1, (IX + d)*
DDCB d 4D	BIT 1, (IX + d)*
DDCB d 4E	BIT 1, (IX + d)
DDCB d 4F	BIT 1, (IX + d)*
DDCB d 50	BIT 2, (IX + d)*
DDCB d 51	BIT 2, (IX + d)*
DDCB d 52	BIT 2, (IX + d)*
DDCB d 53	BIT 2, (IX + d)*
DDCB d 54	BIT 2, (IX + d)*
DDCB d 55	BIT 2, (IX + d)*
DDCB d 56	BIT 2, (IX + d)
DDCB d 57	BIT 2, (IX + d)*
DDCB d 58	BIT 3, (IX + d)*
DDCB d 59	BIT 3, (IX + d)*
DDCB d 5A	BIT 3, (IX + d)*
DDCB d 5B	BIT 3, (IX + d)*
DDCB d 5C	BIT 3, (IX + d)*
DDCB d 5D	BIT 3, (IX + d)*
DDCB d 5E	BIT 3, (IX + d)
DDCB d 5F	BIT 3, (IX + d)*
DDCB d 60	BIT 4, (IX + d)*
DDCB d 61	BIT 4, (IX + d)*
DDCB d 62	BIT 4, (IX + d)*
DDCB d 63	BIT 4, (IX + d)*
DDCB d 64	BIT 4, (IX + d)*
DDCB d 65	BIT 4, (IX + d)*
DDCB d 66	BIT 4, (IX + d)
DDCB d 67	BIT 4, (IX + d)*
DDCB d 68	BIT 5, (IX + d)*
DDCB d 69	BIT 5, (IX + d)*
DDCB d 6A	BIT 5, (IX + d)*
DDCB d 6B	BIT 5, (IX + d)*
DDCB d 6C	BIT 5, (IX + d)*
DDCB d 6D	BIT 5, (IX + d)*
DDCB d 6E	BIT 5, (IX + d)
DDCB d 6F	BIT 5, (IX + d)*
DDCB d 70	BIT 6, (IX + d)*
DDCB d 71	BIT 6, (IX + d)*
DDCB d 72	BIT 6, (IX + d)*
DDCB d 73	BIT 6, (IX + d)*
DDCB d 74	BIT 6, (IX + d)*
DDCB d 75	BIT 6, (IX + d)*
DDCB d 76	BIT 6, (IX + d)
DDCB d 77	BIT 6, (IX + d)*
DDCB d 78	BIT 7, (IX + d)*
DDCB d 79	BIT 7, (IX + d)*
DDCB d 7A	BIT 7, (IX + d)*
DDCB d 7B	BIT 7, (IX + d)*
DDCB d 7C	BIT 7, (IX + d)*
DDCB d 7D	BIT 7, (IX + d)*
DDCB d 7E	BIT 7, (IX + d)
DDCB d 7F	BIT 7, (IX + d)*
DDCB d 80	LD B, RES 0, (IX + d)*
DDCB d 81	LD C, RES 0, (IX + d)*
DDCB d 82	LD D, RES 0, (IX + d)*
DDCB d 83	LD E, RES 0, (IX + d)*
DDCB d 84	LD H, RES 0, (IX + d)*
DDCB d 85	LD L, RES 0, (IX + d)*
DDCB d 86	RES 0, (IX + d)
DDCB d 87	LD A, RES 0, (IX + d)*
DDCB d 88	LD B, RES 1, (IX + d)*
DDCB d 89	LD C, RES 1, (IX + d)*
DDCB d 8A	LD D, RES 1, (IX + d)*
DDCB d 8B	LD E, RES 1, (IX + d)*
DDCB d 8C	LD H, RES 1, (IX + d)*
DDCB d 8D	LD L, RES 1, (IX + d)*
DDCB d 8E	RES 1, (IX + d)
DDCB d 8F	LD A, RES 1, (IX + d)*
DDCB d 90	LD B, RES 2, (IX + d)*
DDCB d 91	LD C, RES 2, (IX + d)*
DDCB d 92	LD D, RES 2, (IX + d)*
DDCB d 93	LD E, RES 2, (IX + d)*
DDCB d 94	LD H, RES 2, (IX + d)*
DDCB d 95	LD L, RES 2, (IX + d)*
DDCB d 96	RES 2, (IX + d)
DDCB d 97	LD A, RES 2, (IX + d)*
DDCB d 98	LD B, RES 3, (IX + d)*
DDCB d 99	LD C, RES 3, (IX + d)*
DDCB d 9A	LD D, RES 3, (IX + d)*
DDCB d 9B	LD E, RES 3, (IX + d)*
DDCB d 9C	LD H, RES 3, (IX + d)*
DDCB d 9D	LD L, RES 3, (IX + d)*
DDCB d 9E	RES 3, (IX + d)
DDCB d 9F	LD A, RES 3, (IX + d)*
DDCB d A0	LD B, RES 4, (IX + d)*
DDCB d A1	LD C, RES 4, (IX + d)*
DDCB d A2	LD D, RES 4, (IX + d)*
DDCB d A3	LD E, RES 4, (IX + d)*
DDCB d A4	LD H, RES 4, (IX + d)*
DDCB d A5	LD L, RES 4, (IX + d)*
DDCB d A6	RES 4, (IX + d)
DDCB d A7	LD A, RES 4, (IX + d)*
DDCB d A8	LD B, RES 5, (IX + d)*
DDCB d A9	LD C, RES 5, (IX + d)*
DDCB d AA	LD D, RES 5, (IX + d)*
DDCB d AB	LD E, RES 5, (IX + d)*
DDCB d AC	LD H, RES 5, (IX + d)*
DDCB d AD	LD L, RES 5, (IX + d)*
DDCB d AE	RES 5, (IX + d)
DDCB d AF	LD A, RES 5, (IX + d)*
DDCB d B0	LD B, RES 6, (IX + d)*
DDCB d B1	LD C, RES 6, (IX + d)*
DDCB d B2	LD D, RES 6, (IX + d)*
DDCB d B3	LD E, RES 6, (IX + d)*
DDCB d B4	LD H, RES 6, (IX + d)*
DDCB d B5	LD L, RES 6, (IX + d)*
DDCB d B6	RES 6, (IX + d)
DDCB d B7	LD A, RES 6, (IX + d)*
DDCB d B8	LD B, RES 7, (IX + d)*
DDCB d B9	LD C, RES 7, (IX + d)*
DDCB d BA	LD D, RES 7, (IX + d)*
DDCB d BB	LD E, RES 7, (IX + d)*
DDCB d BC	LD H, RES 7, (IX + d)*
DDCB d BD	LD L, RES 7, (IX + d)*
DDCB d BE	RES 7, (IX + d)
DDCB d BF	LD A, RES 7, (IX + d)*
DDCB d C0	LD B, SET 0, (IX + d)*
DDCB d C1	LD C, SET 0, (IX + d)*
DDCB d C2	LD D, SET 0, (IX + d)*
DDCB d C3	LD E, SET 0, (IX + d)*
DDCB d C4	LD H, SET 0, (IX + d)*
DDCB d C5	LD L, SET 0, (IX + d)*
DDCB d C6	SET 0, (IX + d)
DDCB d C7	LD A, SET 0, (IX + d)*
DDCB d C8	LD B, SET 1, (IX + d)*
DDCB d C9	LD C, SET 1, (IX + d)*
DDCB d CA	LD D, SET 1, (IX + d)*
DDCB d CB	LD E, SET 1, (IX + d)*
DDCB d CC	LD H, SET 1, (IX + d)*
DDCB d CD	LD L, SET 1, (IX + d)*
DDCB d CE	SET 1, (IX + d)
DDCB d CF	LD A, SET 1, (IX + d)*
DDCB d D0	LD B, SET 2, (IX + d)*
DDCB d D1	LD C, SET 2, (IX + d)*
DDCB d D2	LD D, SET 2, (IX + d)*
DDCB d D3	LD E, SET 2, (IX + d)*
DDCB d D4	LD H, SET 2, (IX + d)*
DDCB d D5	LD L, SET 2, (IX + d)*
DDCB d D6	SET 2, (IX + d)
DDCB d D7	LD A, SET 2, (IX + d)*
DDCB d D8	LD B, SET 3, (IX + d)*
DDCB d D9	LD C, SET 3, (IX + d)*
DDCB d DA	LD D, SET 3, (IX + d)*
DDCB d DB	LD E, SET 3, (IX + d)*
DDCB d DC	LD H, SET 3, (IX + d)*
DDCB d DD	LD L, SET 3, (IX + d)*
DDCB d DE	SET 3, (IX + d)
DDCB d DF	LD A, SET 3, (IX + d)*
DDCB d E0	LD B, SET 4, (IX + d)*
DDCB d E1	LD C, SET 4, (IX + d)*
DDCB d E2	LD D, SET 4, (IX + d)*
DDCB d E3	LD E, SET 4, (IX + d)*
DDCB d E4	LD H, SET 4, (IX + d)*
DDCB d E5	LD L, SET 4, (IX + d)*
DDCB d E6	SET 4, (IX + d)
DDCB d E7	LD A, SET 4, (IX + d)*
DDCB d E8	LD B, SET 5, (IX + d)*
DDCB d E9	LD C, SET 5, (IX + d)*
DDCB d EA	LD D, SET 5, (IX + d)*
DDCB d EB	LD E, SET 5, (IX + d)*
DDCB d EC	LD H, SET 5, (IX + d)*
DDCB d ED	LD L, SET 5, (IX + d)*
DDCB d EE	SET 5, (IX + d)
DDCB d EF	LD A, SET 5, (IX + d)*
DDCB d F0	LD B, SET 6, (IX + d)*
DDCB d F1	LD C, SET 6, (IX + d)*
DDCB d F2	LD D, SET 6, (IX + d)*
DDCB d F3	LD E, SET 6, (IX + d)*
DDCB d F4	LD H, SET 6, (IX + d)*
DDCB d F5	LD L, SET 6, (IX + d)*
DDCB d F6	SET 6, (IX + d)
DDCB d F7	LD A, SET 6, (IX + d)*
DDCB d F8	LD B, SET 7, (IX + d)*
DDCB d F9	LD C, SET 7, (IX + d)*
DDCB d FA	LD D, SET 7, (IX + d)*
DDCB d FB	LD E, SET 7, (IX + d)*
DDCB d FC	LD H, SET 7, (IX + d)*
DDCB d FD	LD L, SET 7, (IX + d)*
DDCB d FE	SET 7, (IX + d)
DDCB d FF	LD A, SET 7, (IX + d)*
DDE1	POP IX
DDE3	EX (SP), IX
DDE5	PUSH IX
DDE9	JP (IX)
DDF9	LD SP, IX
DE n	SBC A, n
DF	RST 18h
E0	RET PO
E1	POP HL
E2 n n	JP PO, nn
E3	EX (SP), HL
E4 n n	CALL PO, nn
E5	PUSH HL
E6 n	AND n
E7	RST 20h
E8	RET PE
E9	JP (HL)
EA n n	JP PE, (nn)
EB	EX DE, HL
EC n n	CALL PE, nn
ED40	IN B, (C)
ED41	OUT (C), B
ED42	SBC HL, BC
ED43 n n	LD (nn), BC
ED44	NEG
ED45	RETN
ED46	IM 0
ED47	LD I, A
ED48	IN C, (C)
ED49	OUT (C), C
ED4A	ADC HL, BC
ED4B n n	LD BC, (nn)
ED4C	NEG*
ED4D	RETI
ED4E	IM 0/1*
ED4F	LD R, A
ED50	IN D, (C)
ED51	OUT (C), D
ED52	SBC HL, DE
ED53 n n	LD (nn), DE
ED54	NEG*
ED55	RETN*
ED56	IM 1
ED57	LD A, I
ED58	IN E, (C)
ED59	OUT (C), E
ED5A	ADC HL, DE
ED5B n n	LD DE, (nn)
ED5C	NEG*
ED5D	RETN*
ED5E	IM 2
ED5F	LD A, R
ED60	IN H, (C)
ED61	OUT (C), H
ED62	SBC HL, HL
ED63 n n	LD (nn), HL
ED64	NEG*
ED65	RETN*
ED66	IM 0*
ED67	RRD
ED68	IN L, (C)
ED69	OUT (C), L
ED6A	ADC HL, HL
ED6B n n	LD HL, (nn)
ED6C	NEG*
ED6D	RETN*
ED6E	IM 0/1*
ED6F	RLD
ED70	IN (C)* / IN F, (C)*
ED71	OUT (C), 0*
ED72	SBC HL, SP
ED73 n n	LD (nn), SP
ED74	NEG*
ED75	RETN*
ED76	IM 1*
ED78	IN A, (C)
ED79	OUT (C), A
ED7A	ADC HL, SP
ED7B n n	LD SP, (nn)
ED7C	NEG*
ED7D	RETN*
ED7E	IM 2*
EDA0	LDI
EDA1	CPI
EDA2	INI
EDA3	OUTI
EDA8	LDD
EDA9	CPD
EDAA	IND
EDAB	OUTD
EDB0	LDIR
EDB1	CPIR
EDB2	INIR
EDB3	OTIR
EDB8	LDDR
EDB9	CPDR
EDBA	INDR
EDBB	OTDR
EE n	XOR n
EF	RST 28h
F0	RET P
F1	POP AF
F2 n n	JP P, nn
F3	DI
F4 n n	CALL P, nn
F5	PUSH AF
F6 n	OR n
F7	RST 30h
F8	RET M
F9	LD SP, HL
FA n n	JP M, nn
FB	EI
FC n n	CALL M, nn
FD09	ADD IY, BC
FD19	ADD IY, DE
FD21 n n	LD IY, nn
FD22 n n	LD (nn), IY
FD23	INC IY
FD24	INC IYH*
FD25	DEC IYH*
FD26 n	LD IYH, n*
FD29	ADD IY, IY
FD2A n n	LD IY, (nn)
FD2B	DEC IY
FD2C	INC IYL*
FD2D	DEC IYL*
FD2E n	LD IYL, n*
FD34 d	INC (IY + d)
FD35 d	DEC (IY + d)
FD36 d n	LD (IY + d), n
FD39	ADD IY, SP
FD44	LD B, IYH*
FD45	LD B, IYL*
FD46 d	LD B, (IY + d)
FD4C	LD C, IYH*
FD4D	LD C, IYL*
FD4E d	LD C, (IY + d)
FD54	LD D, IYH*
FD55	LD D, IYL*
FD56 d	LD D, (IY + d)
FD5C	LD E, IYH*
FD5D	LD E, IYL*
FD5E d	LD E, (IY + d)
FD60	LD IYH, B*
FD61	LD IYH, C*
FD62	LD IYH, D*
FD63	LD IYH, E*
FD64	LD IYH, IYH*
FD65	LD IYH, IYL*
FD66 d	LD H, (IY + d)
FD67	LD IYH, A*
FD68	LD IYL, B*
FD69	LD IYL, C*
FD6A	LD IYL, D*
FD6B	LD IYL, E*
FD6C	LD IYL, IYH*
FD6D	LD IYL, IYL*
FD6E d	LD L, (IY + d)
FD6F	LD IYL, A*
FD70 d	LD (IY + d), B
FD71 d	LD (IY + d), C
FD72 d	LD (IY + d), D
FD73 d	LD (IY + d), E
FD74 d	LD (IY + d), H
FD75 d	LD (IY + d), L
FD77 d	LD (IY + d), A
FD7C	LD A, IYH*
FD7D	LD A, IYL*
FD7E d	LD A, (IY + d)
FD84	ADD A, IYH*
FD85	ADD A, IYL*
FD86 d	ADD A, (IY + d)
FD8C	ADC A, IYH*
FD8D	ADC A, IYL*
FD8E d	ADC A, (IY + d)
FD94	SUB IYH*
FD95	SUB IYL*
FD96 d	SUB (IY + d)
FD9C	SBC A, IYH*
FD9D	SBC A, IYL*
FD9E d	SBC A, (IY + d)
FDA4	AND IYH*
FDA5	AND IYL*
FDA6 d	AND (IY + d)
FDAC	XOR IYH*
FDAD	XOR IYL*
FDAE d	XOR (IY + d)
FDB4	OR IYH*
FDB5	OR IYL*
FDB6 d	OR (IY + d)
FDBC	CP IYH*
FDBD	CP IYL*
FDBE d	CP (IY + d)
FDCB d 00	LD B, RLC (IY + d)*
FDCB d 01	LD C, RLC (IY + d)*
FDCB d 02	LD D, RLC (IY + d)*
FDCB d 03	LD E, RLC (IY + d)*
FDCB d 04	LD H, RLC (IY + d)*
FDCB d 05	LD L, RLC (IY + d)*
FDCB d 06	RLC (IY + d)
FDCB d 07	LD A, RLC (IY + d)*
FDCB d 08	LD B, RRC (IY + d)*
FDCB d 09	LD C, RRC (IY + d)*
FDCB d 0A	LD D, RRC (IY + d)*
FDCB d 0B	LD E, RRC (IY + d)*
FDCB d 0C	LD H, RRC (IY + d)*
FDCB d 0D	LD L, RRC (IY + d)*
FDCB d 0E	RRC (IY + d)
FDCB d 0F	LD A, RRC (IY + d)*
FDCB d 10	LD B, RL (IY + d)*
FDCB d 11	LD C, RL (IY + d)*
FDCB d 12	LD D, RL (IY + d)*
FDCB d 13	LD E, RL (IY + d)*
FDCB d 14	LD H, RL (IY + d)*
FDCB d 15	LD L, RL (IY + d)*
FDCB d 16	RL (IY + d)
FDCB d 17	LD A, RL (IY + d)*
FDCB d 18	LD B, RR (IY + d)*
FDCB d 19	LD C, RR (IY + d)*
FDCB d 1A	LD D, RR (IY + d)*
FDCB d 1B	LD E, RR (IY + d)*
FDCB d 1C	LD H, RR (IY + d)*
FDCB d 1D	LD L, RR (IY + d)*
FDCB d 1E	RR (IY + d)
FDCB d 1F	LD A, RR (IY + d)*
FDCB d 20	LD B, SLA (IY + d)*
FDCB d 21	LD C, SLA (IY + d)*
FDCB d 22	LD D, SLA (IY + d)*
FDCB d 23	LD E, SLA (IY + d)*
FDCB d 24	LD H, SLA (IY + d)*
FDCB d 25	LD L, SLA (IY + d)*
FDCB d 26	SLA (IY + d)
FDCB d 27	LD A, SLA (IY + d)*
FDCB d 28	LD B, SRA (IY + d)*
FDCB d 29	LD C, SRA (IY + d)*
FDCB d 2A	LD D, SRA (IY + d)*
FDCB d 2B	LD E, SRA (IY + d)*
FDCB d 2C	LD H, SRA (IY + d)*
FDCB d 2D	LD L, SRA (IY + d)*
FDCB d 2E	SRA (IY + d)
FDCB d 2F	LD A, SRA (IY + d)*
FDCB d 30	LD B, SLL (IY + d)*
FDCB d 31	LD C, SLL (IY + d)*
FDCB d 32	LD D, SLL (IY + d)*
FDCB d 33	LD E, SLL (IY + d)*
FDCB d 34	LD H, SLL (IY + d)*
FDCB d 35	LD L, SLL (IY + d)*
FDCB d 36	SLL (IY + d)*
FDCB d 37	LD A, SLL (IY + d)*
FDCB d 38	LD B, SRL (IY + d)*
FDCB d 39	LD C, SRL (IY + d)*
FDCB d 3A	LD D, SRL (IY + d)*
FDCB d 3B	LD E, SRL (IY + d)*
FDCB d 3C	LD H, SRL (IY + d)*
FDCB d 3D	LD L, SRL (IY + d)*
FDCB d 3E	SRL (IY + d)
FDCB d 3F	LD A, SRL (IY + d)*
FDCB d 40	BIT 0, (IY + d)*
FDCB d 41	BIT 0, (IY + d)*
FDCB d 42	BIT 0, (IY + d)*
FDCB d 43	BIT 0, (IY + d)*
FDCB d 44	BIT 0, (IY + d)*
FDCB d 45	BIT 0, (IY + d)*
FDCB d 46	BIT 0, (IY + d)
FDCB d 47	BIT 0, (IY + d)*
FDCB d 48	BIT 1, (IY + d)*
FDCB d 49	BIT 1, (IY + d)*
FDCB d 4A	BIT 1, (IY + d)*
FDCB d 4B	BIT 1, (IY + d)*
FDCB d 4C	BIT 1, (IY + d)*
FDCB d 4D	BIT 1, (IY + d)*
FDCB d 4E	BIT 1, (IY + d)
FDCB d 4F	BIT 1, (IY + d)*
FDCB d 50	BIT 2, (IY + d)*
FDCB d 51	BIT 2, (IY + d)*
FDCB d 52	BIT 2, (IY + d)*
FDCB d 53	BIT 2, (IY + d)*
FDCB d 54	BIT 2, (IY + d)*
FDCB d 55	BIT 2, (IY + d)*
FDCB d 56	BIT 2, (IY + d)
FDCB d 57	BIT 2, (IY + d)*
FDCB d 58	BIT 3, (IY + d)*
FDCB d 59	BIT 3, (IY + d)*
FDCB d 5A	BIT 3, (IY + d)*
FDCB d 5B	BIT 3, (IY + d)*
FDCB d 5C	BIT 3, (IY + d)*
FDCB d 5D	BIT 3, (IY + d)*
FDCB d 5E	BIT 3, (IY + d)
FDCB d 5F	BIT 3, (IY + d)*
FDCB d 60	BIT 4, (IY + d)*
FDCB d 61	BIT 4, (IY + d)*
FDCB d 62	BIT 4, (IY + d)*
FDCB d 63	BIT 4, (IY + d)*
FDCB d 64	BIT 4, (IY + d)*
FDCB d 65	BIT 4, (IY + d)*
FDCB d 66	BIT 4, (IY + d)
FDCB d 67	BIT 4, (IY + d)*
FDCB d 68	BIT 5, (IY + d)*
FDCB d 69	BIT 5, (IY + d)*
FDCB d 6A	BIT 5, (IY + d)*
FDCB d 6B	BIT 5, (IY + d)*
FDCB d 6C	BIT 5, (IY + d)*
FDCB d 6D	BIT 5, (IY + d)*
FDCB d 6E	BIT 5, (IY + d)
FDCB d 6F	BIT 5, (IY + d)*
FDCB d 70	BIT 6, (IY + d)*
FDCB d 71	BIT 6, (IY + d)*
FDCB d 72	BIT 6, (IY + d)*
FDCB d 73	BIT 6, (IY + d)*
FDCB d 74	BIT 6, (IY + d)*
FDCB d 75	BIT 6, (IY + d)*
FDCB d 76	BIT 6, (IY + d)
FDCB d 77	BIT 6, (IY + d)*
FDCB d 78	BIT 7, (IY + d)*
FDCB d 79	BIT 7, (IY + d)*
FDCB d 7A	BIT 7, (IY + d)*
FDCB d 7B	BIT 7, (IY + d)*
FDCB d 7C	BIT 7, (IY + d)*
FDCB d 7D	BIT 7, (IY + d)*
FDCB d 7E	BIT 7, (IY + d)
FDCB d 7F	BIT 7, (IY + d)*
FDCB d 80	LD B, RES 0, (IY + d)*
FDCB d 81	LD C, RES 0, (IY + d)*
FDCB d 82	LD D, RES 0, (IY + d)*
FDCB d 83	LD E, RES 0, (IY + d)*
FDCB d 84	LD H, RES 0, (IY + d)*
FDCB d 85	LD L, RES 0, (IY + d)*
FDCB d 86	RES 0, (IY + d)
FDCB d 87	LD A, RES 0, (IY + d)*
FDCB d 88	LD B, RES 1, (IY + d)*
FDCB d 89	LD C, RES 1, (IY + d)*
FDCB d 8A	LD D, RES 1, (IY + d)*
FDCB d 8B	LD E, RES 1, (IY + d)*
FDCB d 8C	LD H, RES 1, (IY + d)*
FDCB d 8D	LD L, RES 1, (IY + d)*
FDCB d 8E	RES 1, (IY + d)
FDCB d 8F	LD A, RES 1, (IY + d)*
FDCB d 90	LD B, RES 2, (IY + d)*
FDCB d 91	LD C, RES 2, (IY + d)*
FDCB d 92	LD D, RES 2, (IY + d)*
FDCB d 93	LD E, RES 2, (IY + d)*
FDCB d 94	LD H, RES 2, (IY + d)*
FDCB d 95	LD L, RES 2, (IY + d)*
FDCB d 96	RES 2, (IY + d)
FDCB d 97	LD A, RES 2, (IY + d)*
FDCB d 98	LD B, RES 3, (IY + d)*
FDCB d 99	LD C, RES 3, (IY + d)*
FDCB d 9A	LD D, RES 3, (IY + d)*
FDCB d 9B	LD E, RES 3, (IY + d)*
FDCB d 9C	LD H, RES 3, (IY + d)*
FDCB d 9D	LD L, RES 3, (IY + d)*
FDCB d 9E	RES 3, (IY + d)
FDCB d 9F	LD A, RES 3, (IY + d)*
FDCB d A0	LD B, RES 4, (IY + d)*
FDCB d A1	LD C, RES 4, (IY + d)*
FDCB d A2	LD D, RES 4, (IY + d)*
FDCB d A3	LD E, RES 4, (IY + d)*
FDCB d A4	LD H, RES 4, (IY + d)*
FDCB d A5	LD L, RES 4, (IY + d)*
FDCB d A6	RES 4, (IY + d)
FDCB d A7	LD A, RES 4, (IY + d)*
FDCB d A8	LD B, RES 5, (IY + d)*
FDCB d A9	LD C, RES 5, (IY + d)*
FDCB d AA	LD D, RES 5, (IY + d)*
FDCB d AB	LD E, RES 5, (IY + d)*
FDCB d AC	LD H, RES 5, (IY + d)*
FDCB d AD	LD L, RES 5, (IY + d)*
FDCB d AE	RES 5, (IY + d)
FDCB d AF	LD A, RES 5, (IY + d)*
FDCB d B0	LD B, RES 6, (IY + d)*
FDCB d B1	LD C, RES 6, (IY + d)*
FDCB d B2	LD D, RES 6, (IY + d)*
FDCB d B3	LD E, RES 6, (IY + d)*
FDCB d B4	LD H, RES 6, (IY + d)*
FDCB d B5	LD L, RES 6, (IY + d)*
FDCB d B6	RES 6, (IY + d)
FDCB d B7	LD A, RES 6, (IY + d)*
FDCB d B8	LD B, RES 7, (IY + d)*
FDCB d B9	LD C, RES 7, (IY + d)*
FDCB d BA	LD D, RES 7, (IY + d)*
FDCB d BB	LD E, RES 7, (IY + d)*
FDCB d BC	LD H, RES 7, (IY + d)*
FDCB d BD	LD L, RES 7, (IY + d)*
FDCB d BE	RES 7, (IY + d)
FDCB d BF	LD A, RES 7, (IY + d)*
FDCB d C0	LD B, SET 0, (IY + d)*
FDCB d C1	LD C, SET 0, (IY + d)*
FDCB d C2	LD D, SET 0, (IY + d)*
FDCB d C3	LD E, SET 0, (IY + d)*
FDCB d C4	LD H, SET 0, (IY + d)*
FDCB d C5	LD L, SET 0, (IY + d)*
FDCB d C6	SET 0, (IY + d)
FDCB d C7	LD A, SET 0, (IY + d)*
FDCB d C8	LD B, SET 1, (IY + d)*
FDCB d C9	LD C, SET 1, (IY + d)*
FDCB d CA	LD D, SET 1, (IY + d)*
FDCB d CB	LD E, SET 1, (IY + d)*
FDCB d CC	LD H, SET 1, (IY + d)*
FDCB d CD	LD L, SET 1, (IY + d)*
FDCB d CE	SET 1, (IY + d)
FDCB d CF	LD A, SET 1, (IY + d)*
FDCB d D0	LD B, SET 2, (IY + d)*
FDCB d D1	LD C, SET 2, (IY + d)*
FDCB d D2	LD D, SET 2, (IY + d)*
FDCB d D3	LD E, SET 2, (IY + d)*
FDCB d D4	LD H, SET 2, (IY + d)*
FDCB d D5	LD L, SET 2, (IY + d)*
FDCB d D6	SET 2, (IY + d)
FDCB d D7	LD A, SET 2, (IY + d)*
FDCB d D8	LD B, SET 3, (IY + d)*
FDCB d D9	LD C, SET 3, (IY + d)*
FDCB d DA	LD D, SET 3, (IY + d)*
FDCB d DB	LD E, SET 3, (IY + d)*
FDCB d DC	LD H, SET 3, (IY + d)*
FDCB d DD	LD L, SET 3, (IY + d)*
FDCB d DE	SET 3, (IY + d)
FDCB d DF	LD A, SET 3, (IY + d)*
FDCB d E0	LD B, SET 4, (IY + d)*
FDCB d E1	LD C, SET 4, (IY + d)*
FDCB d E2	LD D, SET 4, (IY + d)*
FDCB d E3	LD E, SET 4, (IY + d)*
FDCB d E4	LD H, SET 4, (IY + d)*
FDCB d E5	LD L, SET 4, (IY + d)*
FDCB d E6	SET 4, (IY + d)
FDCB d E7	LD A, SET 4, (IY + d)*
FDCB d E8	LD B, SET 5, (IY + d)*
FDCB d E9	LD C, SET 5, (IY + d)*
FDCB d EA	LD D, SET 5, (IY + d)*
FDCB d EB	LD E, SET 5, (IY + d)*
FDCB d EC	LD H, SET 5, (IY + d)*
FDCB d ED	LD L, SET 5, (IY + d)*
FDCB d EE	SET 5, (IY + d)
FDCB d EF	LD A, SET 5, (IY + d)*
FDCB d F0	LD B, SET 6, (IY + d)*
FDCB d F1	LD C, SET 6, (IY + d)*
FDCB d F2	LD D, SET 6, (IY + d)*
FDCB d F3	LD E, SET 6, (IY + d)*
FDCB d F4	LD H, SET 6, (IY + d)*
FDCB d F5	LD L, SET 6, (IY + d)*
FDCB d F6	SET 6, (IY + d)
FDCB d F7	LD A, SET 6, (IY + d)*
FDCB d F8	LD B, SET 7, (IY + d)*
FDCB d F9	LD C, SET 7, (IY + d)*
FDCB d FA	LD D, SET 7, (IY + d)*
FDCB d FB	LD E, SET 7, (IY + d)*
FDCB d FC	LD H, SET 7, (IY + d)*
FDCB d FD	LD L, SET 7, (IY + d)*
FDCB d FE	SET 7, (IY + d)
FDCB d FF	LD A, SET 7, (IY + d)*
FDE1	POP IY
FDE3	EX (SP), IY
FDE5	PUSH IY
FDE9	JP (IY)
FDF9	LD SP, IY
FE n	CP n
FF	RST 38h